Following instructions were furnished for use with 
DISSAM.COM


Dissassembler commands etc.

INstruction   do we want instructins to proceed each interogation?

Object file input (is this coming from a disk?)

OFFSET?  offset will generally be 0; is amount required
for program to wrap from true location to 0100 (or wherever
you loaded it;  100 is usual in cp/m stuff)

reader is always NO

format-hex-ascii  will not come up; only for readers


offset  same as above; entered twice

start and end of where you have it  (0100 and endadd from load 
or SID;  inspect end of the thing to see, and put that in.

source file output  usually yes

known data areas    if you say yes, give start, end, hex for
first;  will prompt again; continue until you say no.

after you get an output, you inspect; if you find junk or ascii
stuff, you declare those to be data areas.


The first task is to define data areas.  The ASCII listing is 
useful in doing this.  You can get this with the ascii study in
SID, through dumps, etc.
    A series of meaningless move register to register instructions
are probably ASCII since most printable ascii is 40H to 7fH

Using the cross-reference listing, locate areas that are
referenced by three or more instructions.  They will usually
be+
	i/o routines or vectors
	small utility routines
	frequently used data


2.  Once you have defined the data areas and isolated the
i/o and utility routines, edit the generated source by 
inserting comments, and assemble.  Almost without exception
the UNDEFINEDs will denote one of two things:
	Dynamic instructin modifications

	reference to an undiscovered data area

After the second or third disassembly it's all up to you...